## Slide 1
HARDWARE DESIGN • STRUCTURAL MONITORING
Smart Bridge Health Monitoring and Earthquake Detection System
Hardware architecture for steel and metal bridge monitoring using an ESP32-C3, MPU6050, ADS1115, and PZT sensors.
ESP32-C3
Controller
MPU6050
Motion sensor
ADS1115
ADC module
PZT
Piezo sensor
HARDWARE SIGNAL PATH
PZT
ADS1115
ESP32-C3
MPU6050
Conceptual connection overview

## Slide 2
01 / HARDWARE PURPOSE
Hardware problem and design goals
02 / 12
The prototype must sense movement, capture vibration signals, and deliver usable data to the controller.
Measure movement
Capture acceleration and angular motion using an IMU.
Capture vibration
Use a PZT sensor to respond to vibration or strain-related changes.
Read analog signals
Convert conditioned PZT signals into digital samples using an ADC.
HARDWARE DESIGN GOALS
Compact
Small controller and breakout modules.
Modular
Keep sensors, conversion, and control separate.
Expandable
Allow extra sensor channels later.
Safe
Protect sensor signals before ADC input.

## Slide 3
02 / PARTS AND ROLES
Main hardware components
03 / 12
ESP32-C3 Super Mini
Main controller; reads digital sensor data and transfers it to the software.
MPU6050
6-axis accelerometer and gyroscope; measures acceleration and angular velocity.
ADS1115
16-bit I²C analog-to-digital converter for conditioned PZT signals.
PZT sensor
Piezoelectric element that generates voltage in response to mechanical stress or vibration.
Power and wiring
Regulated supply, common ground, suitable connectors, and strain relief.

## Slide 4
03 / HOW THE MODULES CONNECT
Hardware architecture and signal flow
04 / 12
Two sensing paths feed one controller: digital motion data and conditioned analog piezoelectric data.
MPU6050
Acceleration + gyro
PZT SENSOR
Analog voltage
SIGNAL CONDITIONING
Protection / bias / filter
ADS1115
ADC
ESP32-C3
Reads both paths
MPU6050 and ADS1115 typically share I²C; verify addresses and voltage compatibility.

## Slide 5
04 / CONTROLLER WIRING
ESP32-C3 Super Mini connections
05 / 12
Example wiring map — confirm the exact GPIO labels and pinout for your board version.
Module / signal
ESP32-C3 connection
Purpose / notes
MPU6050 VCC
3V3 (if supported)
Power IMU from a compatible supply
MPU6050 GND
GND
Common ground
MPU6050 SDA
Chosen I²C SDA GPIO
Digital sensor data
MPU6050 SCL
Chosen I²C SCL GPIO
I²C clock
ADS1115 VDD
3V3
Check module specifications
ADS1115 GND
GND
Common ground
ADS1115 SDA / SCL
Same I²C SDA / SCL bus
Shared bus if addresses and wiring are valid

## Slide 6
05 / DIGITAL SENSOR
MPU6050: motion sensing
06 / 12
MPU6050 MODULE
VCC
GND
SDA
SCL
INT (optional)
Accelerometer
Acceleration along X, Y, Z axes.
Gyroscope
Angular velocity around X, Y, Z axes.
Connection notes
SDA and SCL connect to the ESP32-C3 I²C bus. INT is optional if interrupt-driven sampling is used.

## Slide 7
06 / ANALOG SENSING
PZT sensor and ADS1115 signal path
07 / 12
PZT sensor
Mechanical stress or vibration creates a changing electrical signal.
Signal conditioning
Add suitable protection, biasing, and filtering before ADC input.
ADS1115 ADC
Converts conditioned analog voltage into digital samples over I²C.
IMPORTANT ELECTRICAL SAFETY
Do not connect a bare PZT element directly to the ADS1115 without a designed input circuit. Piezo sensors can produce voltage spikes; protect the ADC and keep signals within its allowed range.

## Slide 8
07 / DIGITAL COMMUNICATION
I²C bus: sharing SDA and SCL
08 / 12
ESP32-C3
I²C controller
MPU6050
IMU data
ADS1115
ADC readings
Both modules can share SDA/SCL if addresses differ and pull-ups / voltage levels are compatible.
Verify the address with an I²C scan. MPU6050 often uses 0x68 or 0x69; ADS1115 commonly uses 0x48–0x4B depending on ADDR wiring.

## Slide 9
08 / PHYSICAL INSTALLATION
Sensor placement on a steel bridge
09 / 12
Placement is conceptual; final positions depend on bridge geometry, expected modes, and engineering guidance.
IMU
PZT
PZT
Mount firmly • protect wiring • provide strain relief • label sensor locations • document orientation

## Slide 10
09 / RELIABLE HARDWARE
Power, grounding, and wiring practices
10 / 12
Regulated power
Use a stable supply appropriate for the ESP32-C3 and each breakout.
Common ground
Connect grounds so digital and analog signals share a reference.
Signal protection
Protect the ADS1115 input from excessive or negative PZT voltage spikes.
GOOD BUILD PRACTICE
Keep sensor wires secure and away from noisy power wiring.
Use strain relief so vibration does not loosen connections.
Check polarity and continuity before powering the circuit.
Measure supply voltage before connecting sensitive modules.
Use suitable enclosure and insulation for the test setup.

## Slide 11
10 / BUILD AND VERIFY
Prototype assembly and hardware checks
11 / 12
1
Inspect parts
Check labels, pinouts, and board condition.
2
Wire the IMU
Connect MPU6050 power, ground, SDA, and SCL.
3
Wire the ADC
Connect ADS1115 I²C and conditioned PZT input.
4
Power and scan
Confirm voltage and detect I²C addresses.
5
Test each sensor
Tilt the IMU gently; use safe vibration on PZT test setup.
6
Secure assembly
Mount sensors firmly and document orientation/location.
Before testing: inspect wiring, check common ground, verify input protection, and confirm no pin exceeds its rated voltage.

## Slide 12
HARDWARE SUMMARY
Sense the movement. Capture the signal. Deliver usable data.
The hardware combines an IMU, a piezoelectric sensing path, an ADC, and an ESP32-C3 controller to collect data for the monitoring software.
MPU6050
Digital motion
PZT + ADS1115
Analog vibration
ESP32-C3
Control + transfer
KEY REQUIREMENT
Condition and protect the PZT signal before ADC input.
THANK YOU
Questions & discussion